## Slide 1
IoT Inertial Mesuament Unit Monitoring
Tanawin Siriwan 6203014610060 sec 1
College of industrial technology
Mechatronics Engineering Technology Division
Asst. prof. Dr.Supod Keawkorn

## Slide 2: Topic
Introduction
Object
Scope
Process
Priciple
Test
Problem
Summarize

## Slide 3: Objective
For stutdy how to application VCL/FMX using delphi.
For stutdy how to use delphi connect the controller using TCP/IP.
For design IMU data monitoring system

## Slide 4: Scope
Data monitoring
Transive and resiceve data using TCP/IP
Control 3D opject movment
Loggging data file
Sorted Data in MySQL database
Send data to MQTT
Monitoring on Nod-Red

## Slide 5: IoT Inertial Mesuament Unit Monitoring
TCP/IP

## Slide 6: Arduino
SMD ATmega328P microcontroller. USB Programming facilitated by the CH340. Input voltage: USB 5V, from computer, power bank or standard USB adapter. 500mA (maximum) 3.3V voltage regulator. 0-5V outputs with 3.3V compatible inputs. 14 Digital I/O Pins (6 PWM outputs). 6 Analog Inputs. ISP 6-pin Header. 32k Flash Memory. 16MHz Clock Speed. R3 Shield Compatible. LED array for 5V, 3.3V, TX, RX and all digital pins. On board programmable push button (pin 2, need to configure as INPUT_PULLUP). On board piezo buzzer (pin 8). Utilize USB Micro-B socket.

## Slide 7: Arduino Ethernetsheild
Shield | Name | Arduino® Ethernet Shield Rev 2
 | SKU | A000024
 | Compatibility | UNO, MEGA
Ethernet | Connector | RJ45
 | Controller | W5500
 | Speed | 10/100 Mbps
 | Communication | SPI
 | Internal memory | 32KB
 | Maximum sockets | 8 individual
 | Supported protocols | IPv4, ICMP, TCP, UDP, ARP, IGMP, PPPoE, MQTT
Storage | Micro SD card slot | 
Power | Operating voltage | 5V
Connectors | TinkerKit | Yes, 6x

## Slide 8: GY-91
MPU9250 + BMP280 module (Three-axis gyroscope + triaxial accelerometer + triaxial magnetic field + pressure) Module Model: GY-91 Use chip: MPU-9250 + BMP280 Power supply: 3-5v (internal low dropout regulator) Communication: standard IIC / SPI communications protocol -Chip 16bit AD converter, 16-bit data output Gyroscopes range: ± 250 500 1000 2000 ° / s Acceleration range: ± 2 ± 4 ± 8 ± 16g Field range: ± 4800uT Pressure range: 300-1100hPa

## Slide 9: Arduino I2C Connected IMU

## Slide 10: Arduino I2C Connected IMU

## Slide 11: Arduino I2C Connected IMU
Arduino IP
Delphi Connected

## Slide 12: Imprementation On FMX Application

## Slide 13: Delphi Conect Arduino Using TCP/IP
Server
Client
TCP/IP

## Slide 14: Delphi TCP/IP Connected Controller

## Slide 15: Delphi Start System
Click

## Slide 16: Delphi Extrax Data

## Slide 17: Delphi Plot Graph

## Slide 18: Graph In FMX Application

## Slide 19: Graph In FMX Application
Acceleration XYZ
Acceleration Norm
Gyro XYZ

## Slide 20: Graph In FMX Application
Magnetrometer Horizontal
Magnetrometer XYZ
Temp & Pressure

## Slide 21: Delphi Store Data Using MySQL

## Slide 22: Delphi Record Data Using MySQL

## Slide 23: MySQL Database Result

## Slide 24: MySQL Database Result

## Slide 25: Delphi ini File

## Slide 26: Delphi Data Logging

## Slide 27: Delphi Data Logging

## Slide 28: Delphi Data Logging

## Slide 29: Datavisualization Using Node-RED
Broker
Publicer
Subscriber

## Slide 30: Delphi Conect MQTT

## Slide 31: Delphi Connect MQTT

## Slide 32: Delphi Connect MQTT
Publicer
Subscriber

## Slide 33: Delphi Connect MQTT

## Slide 34: Form Creat & Close

## Slide 35: Hive MQTT

## Slide 36: Node-Red Extrax Data

## Slide 37: Datavisualization Using Node-RED

## Slide 38: Datavisualization Using Node-RED

## Slide 39: IoT Inertial Mesuament Unit Monitoring

## Slide 40: Problem

## Slide 41: Applied
Delploy Other Device
Monitoring Real Machine

## Slide 42
THE END THX